## Slide 1
OBLIQUE AXIAL ALONG TANDEM
2mm Axially along Tandem
Thickness
INPLANE VIEW = NATIVE VIEW
SCAN AXIALLY ALONG THE TANDEM DIRECTION, SLICES SHOULD BE 2mm THICK, SEE THE FOV NECESSARY
SAGITAL AND CORONAL SCANS SHOULD HAVE THE SAME FOV/ORIGIN.. SEE NEXT PAGE
SCAN1 = T2 TSE OBLIQUE = AXIAL ALONG TANDEM (2mm)
Slice Direction

## Slide 2
OBLIQUE SAGITTAL ACROSS TANDEM
3mm Slice Thickness, Scanning Sagittally With SAME FOV as SCAN1
INPLANE VIEW = NATIVE VIEW
SCAN Sagittally across THE TANDEM DIRECTION, SLICES SHOULD BE 3mm THICK use the same FOV as Scan 1
SCAN2 = T2 TSE OBLIQUE SAGITTAL ACROSS TANDEM (3mm)
(3mm)
Slice Direction

## Slide 3
OBLIQUE CORONAL ACROSS TANDEM
Slice Direction
SCAN3 = T2 TSE Oblique Coronal, Scan Coronally across THE TANDEM, SLICES SHOULD BE 3mm THICK use the same FOV as Scan 1 and Scan 2
(3mm)
Slice Direction
INPLANE VIEW = NATIVE VIEW